## Slide 1
Double Resonance Experiments

## Slide 2
It is often advantageous to reverse or remove the splitting caused by spin-spin coupling
This is called spin decoupling
Spin decoupling (or just “decoupling) can be used for several reasons
  - to simplify spectra
  - to assist in identification of coupling between nuclei
  to improve signal-to-noise
How do we decouple spins from one another?
Remember, coupling occurs because the transitions of one spin ( to  or  to ) ensue
when the other (coupled) spin is in either the  or  state
  thus, to observe the coupling of one spin to another, the lifetime of the coupled spin
  in a given state must be long enough for the transitions of the other to occur
  this lifetime (t1) must be greater than 1/J (J is the scalar coupling constant)
        1 > 1/J
  if this lifetime is significantly shortened, the coupling (splitting of the signal) will not
  be observed
Spin Decoupling
Two main types of decoupling: selective and broad-band

## Slide 3
  selective decoupling
- selective excitation is accomplished by a very long pulse centered at the
Larmor frequency of the signal of interest (remember, the bandwidth is
proportional to 1/τp, so a long pulse is highly selective)
- the long pulse causes rapid    and    transitions such that the lifetime
of any particular spin in any given state is short (i.e. 1 < 1/J)
    selective excitation of one signal (spin) in an NMR spectrum leads to multiplet
    collapse and simplification of the spin-spin splitting patterns of the signals from
    the nuclei to which the spin is coupled
Selective Decoupling
90
d1
1H
1H
low-power long pulse (frequency selective)

## Slide 4
often it is useful to remove all coupling of a given type
for instance, it is often useful in 13C NMR/spectra to remove all coupling from 1H
90
d1
1H
13C
broad-band or “cpd” sequence
Broad-Band Decoupling
  broad-band decoupling (or composite pulse decoupling, cpd)
    - excitation of a large frequency range using a train of short pulses (short pulses
    excite a large bandwidth) applied in rapid succession
- the rapid succession of pulses causes rapid    and    transitions such
that the lifetime of any particular spin in any given state is short (i.e. 1 < 1/J)
    broadband excitation of all frequencies corresponding to a particular nucleus
    type (i.e. all hydrogens) leads to multiplet collapse and simplification of the
    spin-spin splitting patterns of the signals from coupled nuclei

## Slide 5
Selective Spin Decoupling
O
||
CH3-C-O-CH2-CH3
ethyl acetate
trivial example
- selective decoupling of methyl hydrogens from
methylene hydrogens in the ethyl moiety of
ethyl acetate

## Slide 6
selective decoupling can identify signals from coupled nuclei, thus assisting to
establish connectivity/structure
intensities of signals from coupled nuclei are improved (due to multiplet collapse)
- integrals are unchanged for signals from coupled nuclei
selective decoupling
no decoupling
Selective Spin Decoupling

## Slide 7
(right) selective decoupling of the methyl
hydrogens (1.3 ppm) of propylene oxide
confirms identity of signal
from methine H (2.8 ppm)
Selective Spin Decoupling
CH3
H
H
H
O
propylene oxide
(left) selective decoupling of H-6 of
2-chloropyridine leads to assignment
of signals from H-3, H-4 and H-5
2-chloropyridine

## Slide 8
In selective homonuclear decoupling experiments, if the decoupling field is applied during
the acquisition of the FID, signals in the spectrum (‘b’, below) can move relative to their
positions in the control spectrum (‘a’, below) where no decoupling field is applied
This is demonstrated in the spectra shown (below), where the arrow indicates the
frequency at which the decoupling field was applied for spectrum ‘b’
This effect is known as the Bloch-Siegert effect. The shifts in positions of signals are known
as Bloch-Siegert shifts
The effective field experienced by a nucleus is altered by the presence of the decoupling
field, thus causing the frequency changes
It is not observed if the decoupling field is turned off prior to acquisition
If the decoupling field is not too strong
(if B2 << (no – ni)), then the Bloch-Siegert
shifts can be easily calculated:
In many homonuclear (selective) decoupling
experiments, the requirement for selectivity
keeps B2 small, but if B2 is large and is not
turned off during acquisition, Bloch-Siegert
shifts can be very large
Bloch-Siegert Effect
irradiation
frequency
Dn
ni
no
nBS

## Slide 9
- broad-band
1H decoupling
- no decoupling
solvent
Substantial spectral simplification (multiplets collapse to singlets)
Substantial signal-to-noise gains
Signal-to-noise gains arise from two sources:
- collapse of the multiplet into a singlet
- nuclear Overhauser effect (NOE)
The signal-to-noise enhancement by the NOE is not uniform,
so quantitative information is lost
Broad-Band Decoupling
example: acquisition of 13C
spectrum of alpha pinene with
broad-band 1H decoupling

## Slide 10
The nuclear Overhauser effect (NOE) is the change in intensity of the NMR signal from a
nucleus when the spin populations of a nearby nucleus are changed (for instance, by an
electromagnetic pulse)
This is a through space effect (independent of the presence
of a chemical bond)
The effect is distance dependent (upper internuclear
distance limit of 5-6 A); shorter distance, larger effect
The effect is time dependent: it does not develop
instantaneously
The effect is closely tied to relaxation (much more later
in semester)
For broadband decoupling of 1H from 13C:
  the effect (signal-to-noise-enhancement) is proportional to number of 1H nuclei
  attached to a given 13C nucleus
  effect is proportional to density of 1H nuclei (attached or not attached) surrounding
  a given 13C nucleus
  13C signal may be increased up to 200% by nuclear Overhauser effect
  quantitative information lost because relative integral values are dependent on
  the signal-to-noise enhancement by the NOE which is not uniform for all 13C nuclei
Broad-Band Decoupling:
Introduction to the Nuclear Overhauser Effect

## Slide 11
The broadband decoupling or “cpd” sequence can
be as simple as a series of 90 or 180 degree pulses,
or quite sophisticated, employing multiple pulse
angles, multiple pulse phases, and “shaped” pulses
(non-rectangular pulse profiles)
A goal of cpd (composite pulse decoupling) sequence development is to minimize the
effects of pulse imperfections, maximize the exitation bandwith and minimize pulse
power (decoupling pulse strength, or B2 field strength) to avoid problems such as sample
heating
These sequences have “interesting” names, such as MLEV-16 (“Malcolm Levitt”),
WALTZ-16 (“1-2-3, 1-2-3”), GARP (“Globally Optimized Alternating Phase
Rectangular Pulse”), DIPSI-2, SEDUCE, FLOPSY-8, etc.
Examples: MLEV-16, WALTZ-16 and GARP
Broad-Band Decoupling
90
d1
1H
13C
broad-band or “cpd” sequence

## Slide 12
“Decoupling offset profiles” indicate the effective decoupling bandwidth (gB2)
Example: note the bandwidth of GARP is nearly twice that of WALTZ-16
Broad-Band Decoupling
WALTZ-16
GARP

## Slide 13
Broad-Band Decoupling:
Gated Broad-Band Decoupling
90
d1
1H
13C
gated broad-band decoupling sequence
The gated broad-band decoupling experiment is designed to:
  improve signal-to-noise via the NOE (or nOe)
  retain coupling information (retain signal multiplets)
The NOE develops during the time that decoupling
is performed (during the d1 delay time)
1H-13C coupling returns instantaneously when
decoupling is ceased (just before acquisition), so
coupling information (13C signal splitting due to
attached hydrogens) is present in the spectra
The signal enhancement from the NOE begins to be
lost after decoupling ceases, but the loss depends on
T1 relaxation times, which are generally long for 13C
in small molecules, so losses are minimal
Signal-to-noise enhancement by the NOE is not
uniform for all 13C nuclei, so quantitative
information is lost
So, the gated broad-band decoupling sequence is useful when both high signal-to-noise
(from the NOE) and coupling information (signal splitting) are desired or required

## Slide 14
BROAD-BAND DECOUPLING:
INVERSE (“QUANTITATIVE”) GATED BROAD-BAND DECOUPLING
The inverse gated broad-band decoupling experiment is designed to:
  minimize signal-to-noise enhancement by the NOE
  remove signal splitting (thereby improving signal-to-noise due to multiplet collapse)
The NOE does not develop during d1 because
broad-band decoupling is not applied during this time
1H-13C decoupling commences when acquisition
begins), so there is no signal splitting from 1H-13C
coupling
Acquisition times are kept short to minimize
development of signal-to-noise enhancement from the
NOE that can develop when decoupling is on (i.e.
during acquisition)
Because signal-to-noise enhancement by the NOE is
minimized, quantitative information is available from
integrals of the signals
So, overall, coupling information (signal splitting) is lost, signal-to-noise is improved due
to multiplet collapse, and integration can give reliable quantitative information
90
d1
1H
13C
inverse gated broad-band
decoupling sequence

## Slide 15
Broad-Band Decoupling: Examples
no decoupling
-coupled spectrum, no NOE
gated broad-band decoupling
-coupled spectrum, with NOE
inverse gated broad-band decoupling
-decoupled spectrum, no NOE
broad-band decoupling
-decoupled spectrum, with NOE

## Slide 16
Other Decoupling: Off-Resonance Decoupling
13C spectra are routinely subjected to 1H broad-band decoupling in order to improve
signal-to-noise via the NOE and resolve overlapped signals
This often allows unambiguous identification of individual signals and their chemical shifts
at the expense of loss of coupling information (multiplet structure) useful for identification
of -CH, -CH2, and -CH3 groups
There is a compromise method, “off-resonance” 1H decoupling of 13C spectra. The utility of
this method stems from the following attributes:
  it permits some signal to-noise enhancement via the NOE
  it permits some coupling information to remain in order to assist in identification of
  CH, -CH2, and -CH3 groups
  it also reduces heteronuclear (1H-13C) coupling constants so as to reduce overlap of
  multiplets and thus help resolve individual signals
90
d1
1H
13C
“off-resonance” heteronuclear decoupling
In this off-resonance decoupling method, a low power
(but not too low) 1H “pulse” is applied at some
frequency in the 1H spectral window where there are
no signals (hence, “off” resonance)
Often this is at one edge of the spectrum
In the 13C spectrum, some NOE enhancement is
observed, 1H-13C couplings are reduced, multiplet
structures are (normally) preserved but spectral
overlap (multiplet overlap) is reduced

## Slide 17
Other Decoupling: Off-Resonance Decoupling
1H (‘a’), and 13C (‘b’, ‘c’, and ‘d’) spectra of the ethyl group
of ethylbenzene are shown
As indicated in the 1H spectrum ‘a’, a low power pulse is
applied at approximately -0.2 ppm (indicated in the
spectrum) during the entire experiment
In ‘b’ is shown the normal (no decoupling) 13C spectrum
(note the large 1H-13C couplings in the triplet and quartet)
In ‘c’ is shown the off-resonance decoupled spectrum
  note the decreased 1H-13C coupling constants, and
  how this could be important for spectra where
  multiplets are overlapped
  note the improvement in signal-to-noise from the NOE
In ‘d’ is shown the broad-band decoupled 13C spectrum
The magnitude of the observed 1H-13C coupling constant (Jr,
r for “reduced”) in an off-resonance decoupled spectrum is
related to the actual coupling constant (J), the decoupler
field strength (B2, in Hz) and the frequency offset between
the decoupler field and the 1H signal of interest (Dn, Hz):
the approximation holds only when B2 >> Dn

## Slide 18
1H spectrum
of CHCl3
1H-12C (~99%)
1H-13C (~0.5 %)
1H-13C (~0.5 %)
Other Decoupling: Selective Heteronuclear Decoupling
Decoupling 1H from 13C can also be performed selectively
The frequency of a selected signal in the 1H spectrum is saturated, and the 13C signal of the
13C bound to that hydrogen collapses to a singlet
This is very useful for correlating the signals in the 1H and 13C spectra (deciding which
hydrogens are bound to which 13C nuclei
This is done in a manner very similar to “off-resonance” decoupling, except the decoupling
pulse frequency is “on” some resonance (signal), and the power level generally is lower
It is important that the signal(s) in the 1H spectrum corresponding to 1H bound to 13C are
those that are saturated with the low power 1H pulse (not the 1H-12C signal/peak)
The signal corresponding to 1H-13C is split by 1J1H-13C coupling constant, and the peaks lie
on either side of the 1H-12C peak
These peaks are sometimes called the
“satellite” peaks or “13C-satellite” peaks
90
d1
1H
13C
“selective” heteronuclear decoupling

## Slide 19
Other Decoupling: Selective Heteronuclear Decoupling
In ‘A’ is shown the 1H spectrum of crotonic acid, and the 13C spectrum is shown in ‘B’
If the 13C satellites in ‘A’ corresponding to the methy group are saturated, the upfield
quartet in ‘B’ collapses to a singlet
selective heteronuclear
decoupling of 1H from
13C in methyl group
13C spectrum (no decoupling)
off-resonance decoupling
(1H decoupling frequency
n2 at 7.5 ppm as in figure)
off-resonance decoupling
(1H decoupling frequency
n2 at 0 ppm as in figure)

## Slide 20
OTHER DECOUPLING: SOLVENT (H2O) SUPPRESSION
1H NMR in protonated solvents is problematic
The concentration of H2O in H2O is ~55 M (1H concentration ~110 M)
Signals from other molecules are obscured by the large H2O signal
One way to attenuate the H2O signal is by “decoupling”,
or saturating the resonance (called solvent
suppression by “saturation” or “presaturation”)
A long, selective, low power pulse is used to saturate
selectively the H2O frequency, which
greatly attenuates the signal in the spectrum
90
d1
1H (H2O)
1H
solvent (H2O) suppression
1H NMR spectrum of a 1 mM
solution of a protein molecule
no water suppression
with water suppression